## Slide 1: Development of a GLOF Warning System through Strong Endurance Drone-based Long-Range (LoRa) Communication for the Upper Catchment of the Tista River (Proposal under NIDM Research Project on Disaster Management: Innovation & Action Research)
Presented by
Dr. Manoj Kumar Rana (PI),
Dr. Snehasish Ghosh (Co-PI)
Department of Computing Technologies
SRM Institute of Science and Technology, Kattankulathur, Tamil Nadu, 603203, India

## Slide 2: Problem and Objective
Glacier Lake Outburst Flood (GLOF) | 
Problem | Objective
1. Limitations of existing imagery and barrier of Himalayan region - Low spatial resolution (6-10 m per pixel) - Bad weather condition - Rugged terrain, unavoidable wind speed - Ground based system not suitable - Private satellite images are very costly (10-30$/) | 1. Development of a fixed wing, high endurance drone or UAV 2. Investigating and communicating ice fracturing and glacier lake outburst
2. Conventional mathematical model (e.g. GIS/DEM) - Static based on elevation and slope - Glacier level change, movement not detected - Limited pattern recognition | 3. Developing an ML/AI technique to integrate and analyze from both satellite and drone images
3. Data centric non-comprehensive Early Warning System (EWS) - Monitoring same location in same direction - Long time to predict - Lack of relevance in state and district level | 4. Implementation of a 4G/5G based warning system
Glacier Lake Outburst Flood (GLOF) | 
Problem | Objective
 | 1. Development of a fixed wing, high endurance drone or UAV 2. Investigating and communicating ice fracturing and glacier lake outburst
2. Conventional mathematical model (e.g. GIS/DEM) - Static based on elevation and slope - Glacier level change, movement not detected - Limited pattern recognition | 3. Developing an ML/AI technique to integrate and analyze from both satellite and drone images
3. Data centric non-comprehensive Early Warning System (EWS) - Monitoring same location in same direction - Long time to predict - Lack of relevance in state and district level | 4. Implementation of a 4G/5G based warning system
Upper Tista Basin, Sikkim [Dec 1990]
Upper Tista Basin, Sikkim [Dec 2023]

## Slide 3: Glacial Lake Monitoring and Communication
Image stored in SSD card
4G/5G connection to send instant images at regular intervals
LoRa Connection to control the drone (telemetry)
Lake 2
Lake 3
Lake 4
Drone trajectory over a lake
Camp
Lake 1

## Slide 4: Overall Procedure
Start
Drone and Ground Station Set Up
Flying to the Next Waypoint of the Lake Sequence
Capture and Store Images in Camera SSD Card and Sent to Ground Station
Fly Back to the Landing Site
More Lakes to Survey?
AI/ML Data Processing and Prediction
Vulnerability Beyond Threshold?
Quantization and Labelling Vulnerability
Create maps and Send Email/SMS automatically
End
Yes
No
No
Yes
Mission Planning commands:
(www.ardupilot.org/planner)
- Python programming
- Ground clearance: 450-800 m
- Automatic take-off
- LoRa Setup
- Load waypoints of different glacial lakes
Image store and transmission:
- Co-ordinate of each image from GNSS receiver stored and sent (www.rtklib.com/rtklib.htm)
- Camera triggering in each 60 m distance

## Slide 5: Drone Configuration and Communication
Motor and Controller module
Run the drone
PID controller for smooth flight
Power module
2 16Ah Li-Ion batteries
2-3 hour and 200 km
GPS module
Pixhawk autopilot
Integrate all components
Python programming enabled
Control the airplane as per instruction
(https://pixhawk.org/)
Airspeed Sensor
Telemetry module
Control drone remotely (Drone’s altitude, battery)
Range: 10-12 Km
Use LoRa
Camera module
24 MP, 4K, 1/4000 s shutter speed
1 pixel= 15-20 cm
Auto triggered
LIDAR module
Maintain safe distance
Effective during landing
Remote control module
Range: 1-2 km
Manual operation
15 V
5 V
7.2 V
4G/5G modem
- SIM card enabled and provide internet to drone
Jetson Nano
Small computer
Process images to send to ground server
Drone
USB
Ground station
Internet
Communication
LoRa communication
USB

## Slide 6: Early Warning System
Sentinel-2 and ResourceSat-2 (LISS-IV) data and image
Drone captured data and images
Existing
Instant/Live
Processing through ML/AI models (CNN, Random Forest, Support Vector Machine (SVM))
Glacial Morphometric Parameters:
Hypsometric Integral
Ice Compactness Index
Snout Index, etc.
Glacial Lake Morphometric Parameters:
Volume
Mean Depth
Shoreline Index, etc.
Labelling Glacial Event According to Vulnerability
Zone wise Vulnerability Detection in the Local Settlements Areas in One/More Districts
Auto Email to State and District Level Personnel Body
Broadcast SMS to Local People
Database Creation
Data Processing and Analysis `
Decision Support System Creation
Warning Issuance

## Slide 7
Relevance for State and District
Zero casualties through DRR as per disaster management act
Determination of level of vulnerability and issue a warning at local and district level
  Communication through Email, SMS and Website update to proper Personnel/Body
Forecasting of GLOF for next few days and even weeks
Proposed to conduct GLOF awareness workshop at state level with the help of SRM-SIKKIM campus

## Slide 8: Work Plan
ACTIVITIES | I YEAR |  |  |  | II YEAR |  |  | 
 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12
1. Student selection (UG level), Equipment purchase, Satellite data acquisition |  |  |  |  |  |  |  | 
2. Field visit and data collection: Drone image collection, Database creation, Ground based evidence |  |  |  |  |  |  |  | 
3. Image processing through software: Object detection and image classification |  |  |  |  |  |  |  | 
4. Glacial and glacial lake Morphometric analysis and quantification |  |  |  |  |  |  |  | 
4. ML based model and decision Support System |  |  |  |  |  |  |  | 
5. Early Warning System for GLOF: Monitoring of Dynamic changes of glacial lake, Checking warning at various level, Message broadcasting using 4G/5G network |  |  |  |  |  |  |  | 
6. Report Submission |  |  |  |  |  |  |  | 
7. Research publications and patent work |  |  |  |  |  |  |  | 

## Slide 9: Proposed Budget

## Slide 10: Deliverables and Outcome
A low-cost high endurance drone
  Takeoff and landing in steep terrain
  Sustain against strong katabatic winds
  No unreliable compass used
  Tolerate battery deterioration in low temperature, limited technical support
  Easy drone launch and landing process
An efficient Machine Learning model, determining GLOF
  Much better result than conventional mathematical model
  No dependency on satellite and ground system images
Instant and automatic EWS system
UG student internship supported and GLOF awareness program, organised through SRM Sikkim campus
Project can be extended for land slide and other disaster scenarios

## Slide 11: References
Compendium of Task Force Report on NDMA Guidelines Management of Glacial Lake Outburst Floods (GLOFs) A Publication of the National Disaster Management Authority, Government of India.October 2020, New Delhi.
J. C. Ryan, et al., UAV photogrammetry and structure frommotion to assess calving dynamics at store glacier, a large outlet draining the greenland ice sheet. Cryosphere, vol. 9, 1–11, 2015. doi: 10.5194/tc-9-1-2015.
G. Jouvet, et al., Initiation of a major calving event on the bowdoin glacier captured by UAV photogrammetry. Cryosphere, vol. 11, 911–921, 2017. doi: 10.5194/tc-11-911-2017.
T. R. Chudley, et al., High-accuracy uav photogrammetry of ice sheet dynamics with no ground control. Cryosphere, vol. 13, 955–968, 2019. doi: 10.5194/tc-13-955-2019.
G. Jouvet, et al., In-situ measurements of the ice flow motion at Eqip Sermia glacier using a remotely controlled UAV. Geosci. Instr. Methods Data Syst. Discuss., 1–15, 2019. doi: 10.5194/gi-2019-6.
A. Walter, et al., Calving event size measurements and statistics of Eqip Sermia, Greenland, from terrestrial radar interferometry, Cryosphere Discuss., 1–23, 2019. doi: 10.5194/tc-2019-102.
C. Rohner, et al., Multisensor validation of tidewater glacier flow fields derived from sar intensity tracking, Cryosphere Discuss., 1–27, 2019. doi: 10.5194/tc-2018-278
C. Taylor, et al., Glacial lake outburst floods threaten millions globally, Nat Commun 14, 487, 2023. https://doi.org/10.1038/s41467-023-36033-x
S. Kaushik, et al., Increasing risk of glacial lake outburst flood in Sikkim, Eastern Himalaya, Remote Sensing Applications: Society and Environment, vol. 36, November 2024.
P. Hazra, et al., Assessment of Proglacial Lakes in Sikkim Himalaya, India for Glacial Lake Outburst Flood (GLOF) Risk Analysis using HEC-RAS and Geospatial Techniques, J Geol Soc India, vol. 98, 344–352, 2022. https://doi.org/10.1007/s12594-022-1986-1.
S. Schmidt, et al., Cryosphere hazards in Ladakh: the 2014 Gya glacial lake outburst flood and its implications for risk assessment, Nat Hazards, vol. 104, 2071–2095, 2020. https://doi.org/10.1007/s11069-020-04262-8.

## Slide 12: Thank You!!